| Axe Brue – Coastal Belt Deemed to satisfy fences Within 9m of a Watercourse |
| --- |
| Watercourse Classification | Level of access for maintenance | Fencing solutions deemed to have consent |
| 1. Viewed Rhyne | Maintenance possible from both banks | No permanent or temporary fence is allowed within 9m of the top of the bank on either side except as in 1(b) A temporary post and wire stock fence, no higher than 1200mm, maybe erected 6m from the top of either bank (brink of the watercourse); however, suitable entry and exit gates to and from the maintenance strip are required. The Board will also require the riparian owner to undertake annual cutting/flailing of the 6m area between the top brink of the bank and fence. A temporary electric fence is deemed to have consent, but it must be removed by the riparian owner prior to maintenance, no liability will be accepted for any fence damaged if left erected during the maintenance work. Should a fence fall into a state of disrepair the Board will require its repair or renewal by the riparian owner. Failure to comply with the Board’s request may result in the removal of the fence by the Board’s contractors and associated costs reclaimed from the riparian owner |
| 2. Viewed Rhyne | Maintenance possible from one bank only NB: schemes leave a hedge on one bank so maintenance is from one bank only. | No permanent fence is allowed within 9m of the top of the bank (brink of the watercourse) on the working side. A temporary electric fence is deemed to have consent, but it must be removed by the riparian owner prior to maintenance, no liability will be accepted for any fence damaged if left erected during the maintenance work. A temporary post and one strand ?? wire stock fence, no higher than 1200mm, maybe erected 6m from the top of the maintained bank (brink of the watercourse); however, suitable entry and exit gates to and from the maintenance strip are required. The Board will also require the riparian owner to undertake annual cutting/flailing of the 6m area between the top brink of the bank and fence. A temporary post and one strand wire stock fence may be erected within ?? 1.0 metre of the top of the rhyne bank (brink of the watercourse) on the non–maintained side. However, the Board will not be liable for any damage caused to the fence during maintenance work and should the Board require access to the channel, the fence must be removed at the expense of the riparian owner Should a fence fall into a state of disrepair the Board will require its repair or renewal by the riparian owner. Failure to comply with the Board’s request may result in the removal of the fence by the Board’s contractors and associated costs reclaimed from the riparian owner. |
| 3. Non Viewed Rhynes | No maintenance | Temporary post and wire stock fence, no higher than 1200mm , are deemed to have consent but if the Board takes the watercourse into view, fences may need to be removed at the Board’s expense and will not be replaced. The approach under “Section 1. Viewed Rhynes will then apply.” |
| 4. Non Viewed Rhynes | Emergency work or one off maintenance | If the Board’s contractors remove a fence to enable them to carry out maintenance work that should be done by riparian maintenance work, the riparian owner will be responsible for the replacement of any fence removed. |

| Axe Brue – Peat Moors Deemed to satisfy fences within 9m of a Watercourse |
| --- |
| Watercourse Classification | Level of access for maintenance | Fencing solutions deemed to have consent |
| 1. Viewed Rhyne | Maintenance possible from both banks | A temporary electric fence is deemed to have consent, but it must be removed by the riparian owner prior to maintenance, no liability will be accepted for any fence damaged if left erected during the maintenance work. No temporary or permanent fence is allowed within 9m of the top of the either bank where the watercourse is sufficiently wide and deep enough to act as a wet fence. Where (b) does not apply then (c) applies A temporary post and 1 strand wire stock fence less than 1 metre high may be erected 0.75 metres from the top of the rhyne bank (brink of the watercourse) on the maintained side. However, the Board will not be liable for any damage caused to the fence during maintenance work and should the Board require access to the channel, the fence must be removed at the expense of the riparian owner Outside of areas where SSSI management agreements are in place, a temporary post and wire stock fence, no higher than 1200mm, maybe erected 6m from the top of either bank (brink of the watercourse); however, suitable entry and exit gates to and from the maintenance strip are required. The Board will also require the riparian owner to undertake annual cutting/flailing of the 6m area between the top brink of the bank and fence. Should a fence fall into a state of disrepair the Board will require its repair or renewal by the riparian owner. Failure to comply with the Board’s request may result in the removal of the fence by the Board’s contractors and associated costs reclaimed from the riparian owner. |
| Watercourse classification | Level of access for maintenance | Fencing solutions deemed to have consent |
| 2. Viewed Rhyne | Maintenance possible from one bank only NB: schemes leave a hedge on one bank, so maintenance is from one bank only. | No permanent fence allowed within 9m of the top of the brink of either bank. A temporary electric fence is deemed to have consent, but it must be removed by the riparian owner prior to maintenance, no liability will be accepted for any fence damaged if left erected during the maintenance work. A temporary post and wire stock fence, no higher than 1200mm, erected 6m from the top of the maintained bank (brink of the watercourse); however, suitable entry and exit gates to and from the maintenance strip are required. The Board will also require the riparian owner to undertake annual cutting/flailing of the 6m area between the top brink of the bank and fence. A temporary post and wire stock fence (as in 2.c) above) may be erected within 1.0 metre of the top of the rhyne bank (brink of the watercourse) on the non–maintained side. However, the Board will not be liable for any damage caused to the fence during maintenance work and should the Board require access to the channel, the fence must be removed at the expense of the riparian owner Should a fence fall into a state of disrepair the Board will require its repair or renewal by the riparian owner. Failure to comply with the Board’s request may result in the removal of the fence by the Board’s contractors and associated costs reclaimed from the riparian owner. |
| 3. Non Viewed Rhynes | No maintenance | Temporary post and wire stock fence, no higher than 1200mm , are deemed to have consent but if the Board takes the watercourse into view, fences may need to be removed at the Board’s expense and will not be replaced. The approach under “Section 1. Viewed Rhynes will then apply.” |
| 4. Non Viewed Rhynes | Emergency work or one off maintenance | If the Board’s contractors remove a fence to enable them to carry out maintenance work that should be done by riparian maintenance work, the riparian owner will be responsible for the replacement of any fence removed. |

| Axe Brue – Upland areas Deemed to satisfy fences within 9m of a Watercourse |
| --- |
| Watercourse Classification | Level of access for maintenance | Fencing solutions deemed to have consent |
| 1. Viewed Rhyne | Alternating Maintenance from both banks | No permanent fence allowed within 9m of the top of the brink of either bank. A temporary post and wire stock fence, no higher than 1200mm, maybe erected 6m from the top of either bank (brink of the watercourse); however, suitable entry and exit gates to and from the maintenance strip are required. The Board will also require the riparian owner to undertake annual cutting/flailing of the 6m area between the top brink of the bank and fence. A temporary post and 1 strand wire stock fence less than 1 metre high may be erected 1 metre from the top of the rhyne bank (brink of the watercourse) on the maintained side. However, the Board will not be liable for any damage caused to the fence during maintenance work and should the Board require access to the channel, the fence must be removed at the expense of the riparian owner A temporary electric fence is deemed to have consent, but it must be removed by the riparian owner prior to maintenance, no liability will be accepted for any fence damaged if left erected during the maintenance work. Should a fence fall into a state of disrepair the Board will require its repair or renewal by the riparian owner. Failure to comply with the Board’s request may result in the removal of the fence by the Board’s contractors and associated costs reclaimed from the riparian owner |
| Watercourse classification | Level of access for maintenance | Fencing solutions deemed to have consent |
| 2. Viewed Rhyne | Maintenance from one bank only NB: new schemes leave one hedge in, so maintenance is from one bank only. | A temporary electric fence is deemed to have consent, but it must be removed by the riparian owner prior to maintenance, no liability will be accepted for any fence damaged if left erected during the maintenance work. A temporary post and 1 strand wire stock fence less than 1 metre high may be erected 1 metre from the top of the rhyne bank (brink of the watercourse) on the maintained side. However, the Board will not be liable for any damage caused to the fence during maintenance work and should the Board require access to the channel, the fence must be removed at the expense of the riparian owner A temporary post and wire stock fence, no higher than 1200mm, maybe erected 6m from the top of the maintained bank (brink of the watercourse); however, suitable entry and exit gates to and from the maintenance strip are required. The Board will also require the riparian owner to undertake annual cutting/flailing of the 6m area between the top brink of the bank and fence. Should a fence fall into a state of disrepair the Board will require its repair or renewal by the riparian owner. Failure to comply with the Board’s request may result in the removal of the fence by the Board’s contractors and associated costs reclaimed from the riparian owner. |
| 3. Non Viewed Rhynes | No maintenance | Temporary post and wire stock fence, no higher than 1200mm , are deemed to have consent but if the Board takes the watercourse into view, fences may need to be removed at the Board’s expense and will not be replaced. The approach under “Section 1. Viewed Rhynes will then apply.” |
| 4 Non Viewed Rhynes | Emergency work or one off maintenance | If the Board’s contractors remove a fence to enable them to carry out maintenance work that should be done by riparian maintenance work, the riparian owner will be responsible for the replacement of any fence removed. |